## Slide 1
METHANE GAS, ISOTOPES, AND GAS COMPOSITION
Methane Gas – colorless, odorless, flammable
Chemical Composition – 1 atom of carbon and 4 atoms of hydrogen. Also referred to as CH4.
CARBON
“Carbon is the basis of all earth life and is a remarkable element. It makes up both graphite (pencil “lead” one of the softest natural materials) and diamond (one of the hardest natural materials). It also wants to readily bond with other elements (such as hydrogen) and carbon atoms can attach themselves to one another to an extent not possible for atoms of any other element.” Carbon often forms long “chains” and “rings”.
Organic chemistry – the chemistry of the compounds of carbon.
Inorganic chemistry – the chemistry of compounds derived from minerals.

## Slide 2
Methane – CH4
Ethane – C2H6
Propane – C3H8
Butane – C4H10
Pentane – C5H12
Carbon “Chains”

## Slide 3
Carbon “Rings” - Aromatics
Benzene – C6H6
Naphthalene – C10H8

## Slide 5: STABLE ISOTOPES ARE USEFUL TOOLS USED TO DETERMINE THE ORIGIN OF FLUIDS AND GASES.
WHAT IS A STABLE ISOTOPE?
Many elements can exist in different forms known as isotopes. They differ in the number of neutrons
in the nucleus but do not differ in the number
of protons. Stable isotopes are not radioactive.
Carbon Isotopes:
Isotope
12C
13C
14C
Protons
6
6
6
Neutrons
6
7
8
Abundance
98.98%
1.11%
trace
Type
Stable
Stable
Unstable
Hydrogen
Isotopes
Source: A. Gorody, 2004
Notes: The stable carbon and deuterium isotopes of methane (CH4) are used in the oil and gas industry as a diagnostic tool to determine methane origin. Methane originating from the burial of organic sedimentary matter at high temperatures and pressures is defined as thermogenic. Methane originating from bacterial fermentation or from the bacterially-mediated reduction of carbon dioxide is defined as biogenic. Biogenic methane is a common constituent of groundwaters around the world. Approximately 20% of the world’s commercial natural gas reserves is biogenic.

## Slide 6
METHANE GAS, ISOTOPES, AND GAS COMPOSITION
Stable isotopes of carbon and hydrogen are measured relative to a standard.
- delta notation used to describe the difference between the measured ratios of the sample and the reference standard.
The measured ratio is express in parts per mill (1/1000) by the notation 0/00.
 =
X 1000 (‰)
Rsample – Rstandard
Rstandard
999
g
1000
g
Standard
Sample
-1 (‰)
Taken from Beeunas, 2004

## Slide 7
METHANE GAS, ISOTOPES, AND GAS COMPOSITION
The carbon reference standard is either PDB (PeeDee belemnite) (from the National Institute of Standard and Technology, Maryland), Or the VPDB – Vienna PDB (International Atomic Energy Agency, Vienna, Austria).
The hydrogen reference standard is either SMOW (standard mean ocean water) or VSMOW (Vienna standard mean ocean water).
Most analyses can determined to a precision of 0.5 ‰ or better.

## Slide 8
ISOTOPE RATIO MASS SPECTROMETER (IRMS) SCHEMETIC
Source: Clark and Fritz, 1997

## Slide 10
Why look at the stable isotopes of carbon and hydrogen in methane gas?
Major components of petroleum hydrocarbons (example - Methane [CH4])
Carbon system involves both inorganic and organic processes.
Many of the natural carbon processes involve bacteria.
Bacteria are isotopically selective – prefer to metabolize organic material at the weaker, “light isotope (12C)” carbon bonds. Bacteria mediated reactions with carbon lead to large isotope fractionation between 12C and 13C. Also the bacteria mediated reactions involving carbon compounds proceed in one direction only.
The result is that carbon and hydrogen isotope ratios from bacteria related processes become “lighter”.
METHANE GAS, ISOTOPES, AND GAS COMPOSITION

## Slide 11
Chart Source: IsoTech Laboratories, Inc.
VPDB
VSMOW

## Slide 14
Gas Composition Comparisons
Thermogenic methane gas is commonly found with other larger carbon chain gasses (such as, propane, butane, pentane, etc.).
Biogenic methane gas is almost exclusively methane gas - often all methane or with minor amounts of ethane.
Gas composition data when compared with stable isotope results are used together to identify the source of methane gas in waters.
METHANE GAS, ISOTOPES, AND GAS COMPOSITION

## Slide 15
Hydrocarbon Gas Composition
%C2+ “Wetness” Amount of Light Hydrocarbons Relative to Methane
C1 – Methane
C2 – Ethane
C3 – Propane
iC4 – Iso butane
nC4 – Normal butane
METHANE GAS, ISOTOPES, AND GAS COMPOSITION
Methane CH4
Ethane C2H6
Propane C3H8
Butanes
Pentanes
nC4H10
iC4H10
nC5H12
iC5H12
Basic Components of Natural Gases

## Slide 17
Comparison Plot - Sum of C4/C5 vs. Sum C2/C3

## Slide 18
Major Sources of Methane